## Slide 1: By Design Approach in Biomarker Development, Validation, and Clinical Implementation
Zhen Zhang
Center for Biomarker Discovery and Translation
Johns Hopkins University School of Medicine

## Slide 2: Disclosure
Through license agreements between Johns Hopkins University and Vermillion Inc., Dr. Zhen Zhang is entitled to royalty payment from OVA1 and Overa.
The two FDA cleared tests OVA1 and Overa were developed partially supported by a sponsored research agreement between Vermillion Inc. and Johns Hopkins University and funding from DOD and NCI/EDRN.
Clinical performance of the two tests will not be discussed.

## Slide 3: Development of IVDMIA
Biomarker data
Classification model
Clinical evaluation
Model derivation via machine learning
Clinical Relevance
Statistical Soundness
Regulatory Requirements
Study & experimental design
… …

## Slide 4: Critical elements in IVDMIA design and development
Knowledge of disease
Target population
Sampling
Inclusion/exclusion
Knowledge of biomarkers
Trial population
Designed samples for development
Desired performance
Knowledge of machine learning & statistics
Derivation of IVDMIA models
Knowledge of IVD assay requirements
Knowledge of clinical needs

## Slide 5: By design approach
Identify needs
Product specification
Iterative prototyping
Driven by specifications and external constraints.

## Slide 6: Needs: Develop the right biomarkers
Clinically useful
Safe and effective
Practically & commercially viable

## Slide 7: Intended use and desired clinical performance characteristics

## Slide 8: A test’s intended use is defined by the time point at which it is to be used along a disease process
Prognosis
Predicting response to Tx
Monitoring
Early Detection
Screening
Risk Assessment
Wellness?

## Slide 9: The time point-defined intended use in turns helps to define IVDMIA target population (inclusion/exclusion)
and consider the following:
  If test is positive, what are the options for clinical intervention? Will it likely alter patient outcomes?
  What are the consequence for test false positive/false negative?
  What are the current alternatives in testing for this intended use?
  Availability of samples at this time-point under current gold standard Dx?
  Will a meaningful size of patient population benefit from the test? (potential commercial market size)
  ……

## Slide 10: Specifications: Design a test’s desired performance characteristics
Zhang, Z., & Chan, D. W. (2010). Cancer epidemiology, biomarkers & prevention

## Slide 11: Biomarkers having sufficient discriminatory power with respect to desired performance?

## Slide 12
Marker performance statistically stable - Univariate analysis

## Slide 13
Markers complementary?

## Slide 14
-5
-4
-3
-2
-1
0
1
2
3
4
5
-4
-3
-2
-1
0
1
2
3
4
First PCA Component
Second PCA Component
benign
LMP
ovarian cancer, stage I/II
ovarian cancer, stage III/IV
-5
-4
-3
-2
-1
0
1
2
3
4
-3
-2
-1
0
1
2
3
First PCA Component
Second PCA Component
Performance generalize across multiple independent sites?
Preclinical Studies
five sites, retrospective
Clinical Study
Rigshospitalet, prospective
Preliminary validation with multiple retrospective sets (n = 1,800)
Two large-scale (n>500) multicenter clinical trials validated the findings.

## Slide 15: Iterative Selection: it’s not final until it’s final
376992xruns

## Slide 16: Finalize IVDMIA panel of biomarkers

## Slide 17
Biplot of biomarkers in training data and tentative classifier in projected 2D space

## Slide 18: Derive models towards desired clinical performance

## Slide 19: Imperfect or wrong information and labeling errors
Learning Algorithm
observed phenotypic differences (*may have labeling errors)
Model
Biological System
y
Wrong information
(e.g., confounding factors)
y

## Slide 20: Stability in bias-variance tradeoff feature informativeness + learning efficiency + sample size
Training
Validation
Error
Model Capacity
High Bias
High Variance

## Slide 21: UMSA: a modified learning algorithm for SVM to integrate external knowledge/data in training
Individualized
Softness
Adjustable parameters controls the influence of distribution information
Incorporating additional information into empirical risk minimization:
Data conditional distribution;
Sample quality, etc.

## Slide 22: Resistance to sample labeling error

## Slide 23: Knowledge of disease and clinical reality helps to set realistically achievable error rate
Clinically achievable
Error
Model Capacity
Due to wrong information in data?

## Slide 24: By design model development
Select models with desired performance characteristics
Inclosing performance requirement as a part of cost function in training
Performance “shaping” by combining multiple models.

## Slide 25: Bloxplots of individual markers and IVDMIA

## Slide 26: Cutoff and clinical performance characteristics
0.0
0.2
0.4
0.6
0.8
1.0
0.0
0.2
0.4
0.6
0.8
1.0
Proportion of Test Positives
Performance Metrics
Sensitivity
(% of disease detected)
PPV
Additional cases captured
Enriched PPV over Prevalence
NPV
Specificity
Prevalence
At cutoff=5.0AU, 38.0% of premenopausal samples were positive

## Slide 27: Derive models towards desired analytical performance

## Slide 28: MC estimated analytical performance characteristics of IVDMIA
2
3
4
5
6
7
8
9
10
0
1
2
3
4
5
6
7
8
9
Mean IVDMIA
%CV of IVDMIA

## Slide 29: Interdisciplinary knowledge in IVDMIA development
Knowledge of disease
Target population
Sampling
Inclusion/exclusion
Knowledge of biomarkers
Trial population
Designed samples for development
Desired performance
Knowledge of machine learning & statistics
Derivation of IVDMIA models
Knowledge of IVD assay requirements
Knowledge of clinical needs

## Slide 30: Center for biomarker discovery and translation

## Slide 31: Acknowledgement
JHU
  Current: Daniel W Chan, Lori Sokoll,, Hui Zhang, Jin Song.
  Past: C Nicole Rosenzweig, Jinong Li, Alex Rai, Lily Chen, Bai Zhang.
Collaborators on ovarian cancer biomarker research
  RC Bast, Jr., IJ Jacobs, A Berchuck, C Van Haaften-Day, NF Hacker, HW de Bruijn, AG van der Zee, F Ueland, R Bristow, ET Fung, D Munroe, S Skates.
Funding: NCI/EDRN BRL (D Chan), BDL (Z Zhang), CPTAC (H Zhang, Z Zhang, D Chan), DOD (Z Zhang), and Vermillion Inc.

## Slide 32: Critical elements in IVDMIA design and development
Knowledge of disease
Target population
Sampling
Inclusion/exclusion
Knowledge of biomarkers
Trial population
Designed samples for development
Desired performance
Knowledge of machine learning & statistics
Derivation of IVDMIA models
Knowledge of IVD assay requirements
Knowledge of clinical needs